## Slide 1: Community ENERGY COOPeratives
Grenville Ham and Gareth Ellis
The Green Valleys CIC
www.thegreenvalleys.org

## Slide 2: A bit of history
Common use of hydropower in mills as far back as medieval times for grinding corn, weaving and fodder.
Use of small hydroelectric power plant to supply communities and industry in early 1900’s

## Slide 3: Carew Tidal Mill

## Slide 4: Big engineering

## Slide 5: Very big engineering

## Slide 6: Post 2010 – sub 100kW, high head, run-of-river schemes

## Slide 7: The Green Valleys CIC
  Established in 2009
  Not for Profit Community Interest Company
  Designed and Built over 70 Hydropower schemes
  Established Hydropower Turbine Manufacturer
  17 Woodland Groups
  Dozens of Community Groups Supported
  Food growing Initiatives
  Woodfuel / Charcoal enterprises
  Local Apple Juice and Cider Business
  Energy Local Model (Buying and Selling Electricity Locally)
  Advice and energy efficiency

## Slide 8: Hydro – High Head
Notes: 1kW = 2 homes, Domestic energy

## Slide 9: HydroPower

## Slide 10: HYDROPOWER

## Slide 11: Cardiff UnI research – Small Hydro

## Slide 12: Cardiff UnI research – ComMUNITY Hydro

## Slide 13: Woodlands

## Slide 14: Woodland Products

## Slide 15: Community Owned ELECTRIC CARS

## Slide 16: Establishing a LOCAL ENERGY MARKET

## Slide 17: DEVELOPING The LOCAL MARKET
.

## Slide 18: Licences, consents and approvals for hydropower
Abstraction licence (Water Resources Act)
Impoundment licence (Water Resources Act)
Flood Risk Activity Permit (FRAP) (/Env Permitting Regs)
Ordinary Watercourse Consent (OWC) (LLFA)
Fish pass approval
Consent for working in a protected site (SACs/SSSIs)
Protected species licensing
Felling licence
Flood Consequences Assessment (T&C Planning)

## Slide 19: Low impact abstraction regime
NRW Guidance - introducing the flow split
Zoning – 10%, 40%, 50% and 70% take
Maintains flow variability in the low/medium flow range
Important for ecology and geomorphological processes

## Slide 20: Design components - passive hydraulic control
Abstraction flow
Residual flow (% take)
Low flow notch

## Slide 21: Disruption to ecosystem connectivity and geomorphological processes

## Slide 22: Management Zones 2 & 3
Zone 2
<10% gradient
Zone 3
>10% gradient
Based on simple geomorphological classification

## Slide 24: Low impact siting and design principles
Consider geomorphological setting of any structure location – ‘siting’
Work with nature - replicate / mimic natural features
Site within confined channel / valley
Steep bed gradient
Select stable bed and bank material
Select straight river reaches
Avoid active river reaches
Place at or below break of channel slope
Locate downstream of nearby inflows/tributary

## Slide 25: Site intakes at natural steps
Every site is different and must be considered individually

## Slide 26: Minimise impact on sediment transport

## Slide 27: Screening (High Head/Zone 3)
Screening for high head, run-of-river hydropower
Majority of intakes use 1 to 2 mm Coanda screen or perforated plate.
Plunge pool is required downstream

## Slide 28: Screening (Low Head/Zone 2)
More complex depending on species and life stage present
Majority of Zone 2 sites will support juvenile salmonids and be on a migration route
Screening down to 6 or 10 mm
Approach velocities
Bywash (safe downstream route)

## Slide 29: Fish passage
Migratory species – Atlantic salmon, sea trout (Sewin) and eel
BUT all species migrate to complete their lifecycles
HEP intakes can present barriers to fish migration and so lead to habitat fragmentation
Salmon and Freshwater Fisheries Act (1975)
The Eels (England and Wales) Regulations 2009
Water Framework Directive
Environment (Wales) Act 2016

## Slide 30: Fish passage
Migratory salmonids
Technical fish pass – requires Formal Fish Pass Approval from NRW (SAFFA)
Detailed engineering design – included in permits

## Slide 31: Fish passage
Migratory salmonids – existing weir

## Slide 32: Generic design

## Slide 33: Fish passage
Fish passage easement for resident brown trout
Fish passage easement

## Slide 34: Eel passage – boss type

## Slide 35: ANY QUESTIONS?